Name__________________________________Date_____________   ____

Period__________________________________          Points available:	   20

Physics

Worksheet – Centripetal Problems

- In the following situations, identify what force is acting as the centripetal force.

  - A car going around a corner______________________________

  - An airplane flying in a horizontal circle__________________________

  - An airplane pulling out of a vertical dive__________________________

  - A car going very quickly over the crest of a hill________________________

- Why do airplanes bank when they turn?

______________________________________________________________________________________________________________________________________________________

___________________________________________________________________________

_________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- You are swinging a can at the end of a string horizontally over your head.  In what direction is the net force acting on the can?

___________________________________________________________________________

______________________________________________________________________________________________________________________________________________________

___________________________________________________________________________

- Twin sisters are on a merry-go-round.  Jane is riding on the outside row and Mary is riding on the row inside her.  Which twin has the greater centripetal force acting on them?

___________________________________________________________________________

______________________________________________________________________________________________________________________________________________________

___________________________________________________________________________

___________________________________________________________________________

___________________________________________________________________________

- A boy is swinging a 1.6 kg toy plane around his head on a string.  The string is 2.4 m long.  If the speed of the plane is 4.3m/s, how hard is the boy pulling on the rope?

- How fast can the boy swing the plane in the previous problem if the maximum tension the rope can withstand without breaking is 30 N?

- What is the fastest a 1,350 kg car can go around corner with a radius of 64 m if the μs is .75?

- A 54 kg boy is sitting on the floor of a merry-go-round with a radius of 4.3 m.  The merry-go-round is just starting and is slowly speeding up.  Right when the boy gets to a speed of 5.7 m/s, the boy begins to slide off the ride.  What is μs between the boy and the floor?

- A space station has a radius of 37 m.  How fast must it rotate to recreate 1g at the outer edge?(1g is equal to the acceleration due to gravity)